## Slide 1
Factory Automation and Control Methods
Lecture 2: Manufacturing Operations
Daro VAN
Paragon International University
Faculty of Engineering
Department of Industrial Engineering

## Slide 2: Outline
Manufacturing Industries and Production
Manufacturing Operation
Production Facilities
Product/Production Relationships
Lean Production

## Slide 3: 1. Manufacturing Industries and products
Primary industries – cultivate and exploit natural resources Ex. Agriculture, mining
Secondary industries – convert output of primary industry to products Ex. Manufacturing, power generation, construction
Tertiary industries – service sector Ex. Banking, education, government, legal services, retail trade, transportation
Classification of Industries

## Slide 4: 1. Manufacturing Industries and products

## Slide 5: 2. Manufacturing industry and products
Process industries, e.g., chemicals, petroleum, basic metals, foods and beverages, power generation
Discrete product (and part) industries, e.g., car, aircraft, appliances, machinery, and their component parts

## Slide 6: 2. Manufacturing Operations
Raw materials
Finished products
Processing and assembly operations
Material handling
Inspection and testing
Coordination and control
Power
Tools
Machines
Labor
Transformation Process
Scrap or
waste

## Slide 7: 2. Manufacturing Operations Processing and Assembly Operation

## Slide 8: 2. Manufacturing Operations Processing Operation
Shaping operations
  Solidification processes
  Particulate processing
  Deformation Processes
  Material removal processes
Properties-enhancing operation (heat treatments)
Surface processing operation
  Cleaning and surface treatments
  Coating and thin-film deposition

## Slide 9: 2. Manufacturing Operations Assembly Operation
Joining processes
  Welding
  Brazing and soldering
  Adhesive bonding
Mechanical assembly
  Threaded fasteners (e.g., bolts and nuts, screws)
  Rivets
  Interference fits (e.g., press fitting, shrink fits)
  other

## Slide 10: 2. Manufacturing Operations Other factory operations
Material handling
Material transport
  Vehicle, e.g., forklift trucks, monorials
  Conveyors
  Cranes…
Storage systems
Unitizing equipment
Automatic identification and data capture
  Bar codes….

## Slide 11: 2. Manufacturing Operations Other factory operations
Time Spent in Material handling

## Slide 12: 2. Manufacturing Operations Other factory operations
Inspection and testing
Inspection – conformance to design specifications
  Inspection for variables – measuring
  Inspection of attribute – gauging
Testing – observing the product (or part, material, subassembly) during operation

## Slide 13: 2. Manufacturing Operations Other factory operations
Coordination and Control
Regulation of the individual processing and assembly operations
  Process control
  Quality control
Management of plant level activities
  Production planning and control
  Quality control

## Slide 14: 3. Production Facilities
Facilities organized in the most efficient way to serve the particular mission of the plant and depends on:
  Type of products manufactured
  Production quantity
  Product variety

## Slide 15: 3. Production Facilities
Production quantity (IQ)
Number of units of a given part or product produced annually by a plant
Three quantity ranges
  Low production – 1 to 100 units
  Medium production – 100 to 10,000 units
  High production – 10,000 to millions of units

## Slide 16: 3. Production Facilities
Production variety (P)
Number of different product or part designs or types
‘Hard’ product variety – products differ greatly
  Few common components in an assembly
‘Soft’ product variety – small differences between products
  Many common components in an assembly

## Slide 17: 3. Production Facilities
Low production quantity
Job shop – makes low quantities of specialized and customized products
Products are typically complex (e.g., specialized machinery, prototypes, space capsules)
Equipment is general purpose
Plant layouts
  Fixed position
  Process layout

## Slide 18: 3. Production Facilities
Medium production quantity
Batch production – a batch of a given product is produced, and then the facility is changed over to produce another product
  Changeover takes time – setup time
  Typical layout – process layout
  Hard product variety
Cellular manufacturing – A mixture of products is made without significant changeover time between products
  Typical layout – cellular layout
  Soft product variety

## Slide 19: 3. Production Facilities
High production
Quantity production – Equipment is dedicated to the manufacturing of one product
  Standard machines tooled for high production (e.g., stamping presses, molding machines)
  Typical layout – process layout
Flow line production – Multiple workstations arranged in sequence
  Product requires multiple processing or assembly steps
  Production layout is most common

## Slide 20: 4. Product/Production Relationships 4.1 Production Quantity and Production Variety
Let = annual quantity of variety ‘’
= variety of product from ‘1’ to ‘’
Total number of product units is defined as
The total number of product models is given by

## Slide 21: 4. Product/Production Relationships 4.1 Production Quantity and Production Variety
The parameter P can be divided into two levels called and . refers to the number of distinct product lines produced by the factory, and refer to the number of models in a product line. The total number of product models is given by

## Slide 22: 4. Product/Production Relationships 4.1 Production Quantity and Production Variety

## Slide 23: 4. Product/Production Relationships 4.1 Production Quantity and Production Variety
Product complexity number of components in product
Part complexity number of processing operations per part

## Slide 24: 4. Product/Production Relationships Factory Operation Model
Simplified
Total number of product units
Total number of parts produced
Total number of operations
Where
P = Production variety
Q = Production quantity
= Number of parts in product
= Number of operations in product

## Slide 25: 4. Product/Production Relationships Factory Operation Model

## Slide 26: 4. Product/Production Relationships Manufacturing Capability
Technological processing capability – the available set of manufacturing processes
Physical size and weight of product
Production capability (plant capability) – production quantity that can be made in a given time

## Slide 27: 4. Product/Production Relationships Lean Production
Utilization of resources – workers, equipment, time, space, materials
Minimizing time
Maximizing quality ( accuracy)
Minimizing cost
Doing more with less, and doing it better
Operating the factory with the minimum possible resources and yet maximizing the amount of work accomplished

## Slide 28: 4. Product/Production Relationships Programs Associated with Lean Production
Just-in-time delivery of parts
Worker involvement
Continuous improvement
Reduced setup times
Stop the process when somethings is wrong
Error prevention
Total productive maintenance

## Slide 29: References
Mikell P. Groover, “Automation, Production Systems and Computer-integrated Manufacturing” , 4th edition, Pearson, chapter 2